## Slide 1: Wifi Security
Nick Kartsioukas

## Slide 2: What’s wifi?
Communicate using the MAGICAL POWER OF THE ÆTHER!
802.11: 1997, 2mbit/sec, 2.4GHz
802.11b: 1999, 11mbit/sec, 2.4GHz
802.11a: 1999, 54mbit/sec, 5GHz
802.11g: 2003, 54mbit/sec, 5GHz
802.11n: 2009, 72-300mbit/sec, 2.4/5GHz
802.11ac: 2013, 100-1300mbit/sec, 5GHz

## Slide 3: What’s a gigzahurt?
Cycles/second (Hertz) of a radio signal
Wifi is channelized, 20/40/80/160MHz wide channels
2.4GHz has 70MHz bandwidth in 11 channels
  Only 3 non-overlapping (1, 6, 11)
5GHz has 665MHz bandwidth, in 45 non-overlapping channels
  30 are DFS, have special requirements to prevent interference with RADAR

## Slide 4: What do I need for teh wifis?
Ad-hoc
Bridged
Infrastructure
  AP
    ESSID
  Client(s)
  All traffic goes via AP

## Slide 5: MOAR DETAIL PLZ
Management frames
  Association request/response, beacon, auth/deauth…
Control frames
  Power save, RTS/CTS…
Data frames
  Payload, QoS, ACKs…
Notes: Important note, management and control frames are not encrypted or signed in any way.

## Slide 6: How do I keep people from mooching?
Security!
  MAC filtering
  WEP
  WPA
  WPA2
Notes: MAC filtering is basically useless

## Slide 7: What’s WEP?
“Wired Equivalent Privacy” (lol)
64/128-bit seed (24-bit IV + 40/104-bit shared key)
RC4 stream cipher
CRC32 integrity check
Open or handshake authentication
“Weaknesses in the Key Scheduling Algorithm of RC4”, Fluhrer, Mantin and Shamir, 2001
  Related key attack, exploits small IV keyspace (16.7M)
  Key recovery in a short time (minutes on a busy network)
Notes: seed -> RC4 -> stream cipher XOR plaintext = ciphertext
Handshake: auth: challenge/response, AP sends random number, client encrypts and sends back. Known plaintext attack, anyone? So, open authentication used instead
2004 paper shows 6.5 days to brute-force a 40-bit RC4 key.

## Slide 8: Well that’s terrible…how about WPA?
“Wifi Protected Access”
Sort of fixes WEP…kinda?
Uses TKIP
  Key mixing instead of straight concatenation
    Dynamic session key
    Session key + IV -> RC4
  Sequence numbering
  64-bit message integrity check
    2 invalid MICs in 60 seconds triggers session key rotation
    Rotation requires a 60-second timeout, DoS anyone?
Notes: Session key is a hash of several values
Hash was expensive on older AP processors, so not done often

## Slide 9: Didn’t you mention WPA2?
Totally new design
CCMP
  Counter Cipher Mode with Block Chaining Message Authentication Code Protocol
  AES block cipher
  PBKDF2 to generate encryption key from PSK
Notes: PBKDF – Password Based Key Derivation Function

## Slide 10: That sounds great!
Well…
WPS
  Wifi Protected Setup
  PIN-based key exchange
Notes: PIN is 8 characters, 1 is checksum, verification is split into 4 and 3 character segments so only have to guess 11,000 values…<4hrs
Usually printed on AP (but physical access == pwned anyway, this is just faster!)

## Slide 11: What about large environments?
802.1x
  LEAP
  PEAP
  EAP-TTLS
  EAP-TLS
Notes: LEAP uses MS-CHAP, known to be weak, Cisco proprietary
PEAP, tunnels EAP (Commonly EAP-MSCHAPv2), similar to EAP-TTLS, uses public server certificate to set up TLS channel
EAP-TTLS, EAP tunneled within TLS, server authenticates to client via TLS and then performs EAP over secure channel, not supported in Win7 and earlier
EAP-TLS, requires client-side certs (so needs PKI set up)

## Slide 12: How are they broken?
aircrack-ng
  WEP, WPA, WPA2
  deauth, replay, injection, fake AP, capture
John the Ripper
  Wordlist
hashcat
  GPGPU brute-forcing
  Wordlist, rule engine
crunch
Notes: Aircrack-ng, full suite of tools for wireless attack
JTR and hashcat to crack captured exchanges
Crunch to generate wordlists

## Slide 13: How do I keep others out?
WEP – Yeah, no chance, don’t use it
WPA – Meh. Why bother?
WPA2 – Long, strong passphrase or random string
  Except “correct horse battery staple”
  pa9ieweesuphaeRoo0eephoo2ahdohgo1IeZ3QuohVoo1ithiel0ooZieng2iec
  COOK^feed&middle_shine!December
WPA2-Enterprise
  PKI + RADIUS

## Slide 14: Where do I learn more?
http://etutorials.org/Networking/802.11+security.+wi-fi+protected+access+and+802.11i/
802.11, 802.1x, and Wireless Security https://www.sans.org/reading-room/whitepapers/wireless/80211-8021x-wireless-security-171
Hacking 802.11 Basics: https://www.youtube.com/watch?v=zxs0sclPEfg
Wireless Pentesting: https://www.youtube.com/watch?v=kMq7uzWY_jI
Aircrack-ng tutorials: http://www.aircrack-ng.org/doku.php?id=tutorial

## Slide 15: Where do I find you?
Twitter, @explodinglemur
github.com/explodinglemur/presentations